## Slide 1: Vulnerability
Report
Security Evaluation on the project of Team3 by Team2(SHEILD)

## Slide 2: Team members and evaluation plan

## Slide 3
Team Member | Role | Schedule
Jin Woo Kim | Project Management, Network system architecture analysis | 
Nam Il Lee | White Box Analysis (Static Analysis) | 
Se Han Yoon | Black Box Analysis (Fuzzing Test) | 
Jang Hyun Ko | System & Security architecture analysis | 
Hoon Min Lee | Network system architecture analysis | 
Ji Hyun Jang | Network system architecture analysis | 
David Belasco | Mentor | 
Team members and evaluation plan

## Slide 4
1
3
5
GATHERING
INFORMATION
EXPLOIT
Q&A
2
4
CONCLUSIONS
ANALYSIS
Contents

## Slide 5
Simple System diagram
This is a simple diagram to understand the relationship between components.
The 2FA part for Admin authentication is omitted.(etc. Google OTP)
After Admin authentication, user account management is possible through the Cockpit Webpage.
The supplied OpenVPN, PAM, and Cockpit SW are widely used open sources.
System Configuration
1.Gathering Information
User
App.
(client)
OpenVPN
Network
PC
WiFi
Network
DemoCannon
(server)
OpenVPN
Network
Rasp.
WiFi
Network
RSA Keys
Robot
PAM

## Slide 6
1. Secure Communication
Using OpenVPN's strong encryption and secure protocol, Sniffing and spoofing from external access is significantly prevented:
Provides a secure network environment for the IP (server IP) requesting connection
Strong Encryption: Supports TLS 1.3 protocol to apply RSA-2048 and AES-256 encryption
Secure protocol: Prevent Replay attacks with a protocol using sequence numbers
Evaluation Constraints
1.Gathering Information
User
App.
(client)
OpenVPN
Network
PC
WiFi
Network
DemoCannon
(server)
OpenVPN
Network
Rasp.
WiFi
Network
RSA Keys
Robot
PAM
IP Address

## Slide 7
2. User Authentication and Management
A strong authentication mechanism by PAM make difficult to takeover account or unauthorized access
  PAM allows for multiple user authentication methods, locking accounts based on number of failed attempts, and enforcing strong password policies.
Evaluation Constraints
1.Gathering Information
User
App.
(client)
OpenVPN
Network
PC
WiFi
Network
DemoCannon
(server)
OpenVPN
Network
Rasp.
WiFi
Network
RSA Keys
Robot
PAM
ID/PW
Pass/Reject
With these two constraints, we focused on only
server and client applications,
key management,
and, network configurations
Untrusted

## Slide 8: Evaluation Narrative
Decide which elements to evaluate
  Static Code Analysis and Fuzzing to find issues not discovered due to SonarQube(team3 used) rule coverage limitations
  Secure data transmission of the client or server application
  Secure storing certificate and private key for TLS connection
  Network configurations for OpenVPN
Select security evaluation techniques
  Wireshark, tcpdump : Network Traffic Analysis
  Boofuzz : Network Fuzzer Testing
  Zmap : network scanning tool that scans port -> No open ports found
  clang-tidy : Static Code Analysis
  ZAP : Web application(Cockpit) security testing tool
1.Gathering Information

## Slide 9: Tool Analysis
1.Static Analysis(with clang_tidy)
3 errors were found.
Client.cpp 395 lines : Format string vulnerability
The other two are not critical but recommended for improvement.
2.OWASP ZAP Scanning Attack
3.OWASP ZAP Fuzzing Test
ZAP scan reported 1 high level risk, but it was a misdetection of tool.
Web application(Cockpit)
It is possible to print internal stack memory using
MT_TEXT message.
2.Analysis
ZAP fuzzer tried 156,117 fuzzing test,
but there was no crash and no successful injection attack.
Web application(Cockpit)

## Slide 10: Data transmission
Insecure data transmission at the client side
2.Analysis
As seen with the constraints, the connection between the server-side OpenVPN and client-side OpenVPN is highly secured. But..
Trusted User
App.
(client)
OpenVPN
Network
PC
WiFi
Network
DemoCannon
(server)
OpenVPN
Network
Rasp.
WiFi
Network
Robot
Sniffer
Untrusted
Communication between the client application and the OpenVPN network is in plaintext and lack of mutual authentication.
Conditions :
1. Trusted user is connected to VPN
2. Untrusted user can access PC
-> Anyone can sniff the data or send commands by packet spoofing.

## Slide 11: Storing certificate and key
Insecure storing certificate and private key
2.Analysis
User
App.
(client)
OpenVPN
Network
PC
WiFi
Network
DemoCannon
(server)
OpenVPN
Network
Rasp.
WiFi
Network
Robot
PAM
OpenVPN uses TLS to perform authentication of the server and client in order to establish a secure channel.
However, the client certificate and private key used for TLS authentication are exposed.
Untrusted
Copy,replace
Conditions :
1. Trusted user is connected to VPN
2. Untrusted user can access client PC
-> Anyone can perform a man-in-the-middle (MITM) attack using a fake CA certificate.

## Slide 12: Storing certificate and key
Insecure storing certificate and private key
2.Analysis
User
App.
(client)
OpenVPN
Network
PC
WiFi
Network
DemoCannon
(server)
OpenVPN
Network
Rasp.
WiFi
Network
Robot
PAM
OpenVPN uses TLS to perform authentication of the server and client in order to establish a secure channel.
However, the client certificate and private key used for TLS authentication are exposed.
-> Anyone can perform a man-in-the-middle (MITM) attack using a fake CA certificate.
Conditions :
1. Trusted user is connected to VPN
2. Untrusted user can access client PC
Untrusted
Man in the Middle

## Slide 13: Network configuration
1.Insecure server authentication
2.Analysis
User authentication is simply replaced with an IP table(OpenVpn IP band). There are No user authentication in server application
-> Anyone can connect to the server and transmit packets by IP spoofing
target prot opt source destination
--------------------------------------------------------------------------------------
ACCEPT tcp -- 10.8.0.0/24 anywhere tcp dpt:5000
IP Tables
Client
eth0 interface:
- ip: 192.168.0.224
vpn interface:
- ip: 10.8.0.5
Server
eth0 interface:
- ip: 192.168.0.248
vpn interface:
- ip: 10.8.0.1
Can't Connect
Connect
Conditions :
1. Untrusted user already known VPN IP address
2.Exposed OpenVPN configuration
The file for OpenVPN configuration is exposed.
-> Anyone can forcefully change the target network
IP and port of the Open VPN connection.

## Slide 14: 3.EXPLOIT
Vulnerabilities
Packet sniffing/spoofing
Sniffing transmitted data and sending a fire command by untrusted user
MITM attack
Client IP spoofing
Establishing a TCP connection with an untrusted user
Intercepting the communication between two parties and sending commands by untrusted user.

## Slide 15
1.Sniffing transmitted data
Wireshark in client PC
#1. Pre-Arm
#2. Armed Manual
#3. Fire
Exploit via Packet sniffing/spoofing
3.Exploit
#1. Pre-Arm packet payload
Python code for sending packets
2.Sending these 3 packets to fire
Transmitted data in plaintext on the client PC using Wireshark.
And, also you can see the addresses and ports for the TCP connection.
Real-time sniffing of seq_num and ack_num of the TCP connection and sending of captured messages is possible.

## Slide 16: Exploit via Packet sniffing/spoofing
3.Exploit
https://youtu.be/oly2VFk9DJY

## Slide 17: Exploit via MITM attack
3.Exploit
1.Replacing certificates and key on client
Copy the certificate and key on the client, and replace them with others.
It makes the client to spoof authentication with the middle server.
2.Modifing OpenVPN configuration file in client.
Modify the OpenVPN configuration file on the client.
This allows ignoring the user's IP input and connecting to the middle server's IP.
3.Forwarding user login to establish OpenVPN connection
By forwarding the user ID and password, the connection can be established.
After that, the middle server can intercept all communications or send any messages.

## Slide 18: Exploit via MITM attack
3.Exploit
Application
OpenVPN Network(C)
Robot
OpenVPN Network(S)
User Device : 192.168.0.123
Robot Device : 192.168.0.248
Connect Request
192.168.0.248
PAM
Input:
192.168.0.248
id : trust
pw : trust123!@#
OpenVPN Network(S)
OpenVPN Network(C)
Connect Request
192.168.0.163:1195
Connect Request
192.168.0.248:1194
Exploit
Program
id : trust​
pw : trust123!@#
Attacker Device : 192.168.0.163
Pass
Config. file
Fake key
Fake key

## Slide 19: Exploit via MITM attack
3.Exploit
https://youtu.be/5gz9pafMpxQ

## Slide 20: Exploit via IP Spoofing
Establishing a TCP connection with an untrusted user
3.Exploit
1. Check the server connection port on the client.
2. Change the attacker's address to the IP band used by OpenVPN.
3. Create a new client and try to connect to the server.
※ Connected to the address assigned by AP using the 10.8.0.X IP

## Slide 21: Conclusions and Recommendations
4. Conclusions
Vulnerability | Mitigation Strategy
Lack of encryption and authentication between endpoints | Use TLS to communicate securely between the client application and server application.
Exposed certificates and keys | Store keys in secure Storage rather than a regular filesystem
Insecure configuration files | Ensure the integrity of some configuration files using hash

## Slide 22: Lessons Learned
4. Conclusions
Although the effective use of open source is impressive, vulnerabilities still exist.
Sharing other people's opinions and various opinions is effective in improvement of security.
It is important to have experience with a variety of analysis tools.
Key protection is always important.
With importance of secure software training, the need for a security mindset has been highlighted.

## Slide 23: THANKS
DO YOU HAVE ANY QUESTIONS?

## Slide 24: VULNERABILITY REPORT
Appendix

## Slide 25: OWASP ZAP ATTACK
Alert type | Risk | Count
Cloud Metadata Potentially Exposed | High | 1(100%)
Information Gathering
ZAP intercepts and analyzes requests and responses to gather information about the target web application's structure and vulnerabilities.
Vulnerability Detection
ZAP identiﬁes various security vulnerabilities such as SQL injection, cross-site scripting (XSS), cross-site
request forgery (CSRF), authentication and session management ﬂaws.
Scanning
ZAP offers automated scanning capabilities to search for vulnerabilities in the target web application using different attack techniques.
ZAP simulates various attack techniques to test the security strength of the web application, helping developers and security teams identify and address weaknesses.
Attack Simulation​
ZAP scan reported 1 high level risk, but it was a misdetection of tool.
Because https://10.8.0.1:9090/latest/meta-data/ responds 200 OK even if it is not an exist page.
Appendix

## Slide 26: OWASP ZAP FUZZING TEST
Automation
ZAP automates the process of sending various inputs to the target application, systematically testing different scenarios to discover vulnerabilities automatically.
Random
ZAP generates random inputs and sends them to the target application, aiming to uncover unexpected behavior or vulnerabilities caused by unexpected data.
Crash
In the context of FUZZING TEST, ZAP attempts to identify input combinations that can cause the target application to crash, hang, or become unresponsive, revealing potential stability or robustness issues.
Injection
ZAP injects malicious or unexpected input values into user inputs, headers, or other parts of the request, aiming to identify vulnerabilities like SQL injection, command injection, or other
injection-related ﬂaws in the target application's handling of user input.
ZAP fuzzer tried 156,117 fuzzing test, but there was no crash or successful injection attack.
Appendix

## Slide 27: ZMAP – Port scan
Zmap Command
Result
Can't find any open ports via zmap.
$> sudo zmap -p 0-65535 -w target.txt --output-module=csv -o port_scan_result.csv --output-fields=saddr,daddr,sport,dport,success --output-filter="success=1 && repeat=0"
saddr,daddr,sport,dport,success
port_scan_result.txt
Appendix